## Slide 1
25AIC115 Introduction to Cyber Physical Systems and Control Theory – 2
Dhiren Vasudeva(CB.AI.U4CPS25014)
Pardhav Reddy(CB.AI.U4CPS25059)
Poovya.S(CB.AI.U4CPS25061)
Ch.Venkata Abhiram(CB.AI.U4CPS25012)
GROUP 9:
“Mini Air Defence System”
PROJECT TITLE:
1

## Slide 2
2
Contents of presentation
1. Introduction
2. Recap
3. Problem Statement
4. Objectives
5. System Architecture
6. Hardware Components Used
7. Software Tools Used
8. Methodology
8. Implementation Setup
9. Results & Observations
10. Applications, Limitations & Future Enhancements
11. Conclusion & Reference

## Slide 3
3
Problem Statement
Traditional security systems either detect everything blindly (ultrasonic) or require constant human monitoring. There is a need for an intelligent, low-cost system that can identify specific threat objects, distinguish safe targets, and trigger a response automatically or on command — with remote notification capability.

## Slide 4
4
Introduction
Mini Air Defence System is a smart detection and response system designed to identify specific objects and trigger an action.
Objective
  Detect specific objects using computer vision
  Improve previous ultrasonic-based detection system
  Provide manual override shooting mechanism
Applications
  Civilian security areas
  Small military camps
  Restricted zones

## Slide 5
5
Real World Air Defence Systems
Modern air defence systems operate on similar principles but with advanced technology.
Examples include:
• Iron Dome (Israel) – intercepts short-range rockets
• Patriot Missile System (USA) – surface-to-air missile defense
• S-400 (Russia) – long-range air defense system
Our prototype demonstrates the basic working concept of these systems using low-cost components.

## Slide 6
6
Previous Semester Work
System Components
  Ultrasonic Sensor
  Servo Motor
  Microcontroller
  Trigger Mechanism
Working
  Detect object using ultrasonic distance
  Rotate servo motor
  Activate shooting mechanism
Limitations
  Cannot identify objects
  Detects all obstacles
  Not intelligent detection

## Slide 7
7
Improvements in Current Semester
New features added:
  Camera module for vision
  YOLOv11 object detection
  Detection of specific objects:
    Mobile Phone
    ID Card
    Water Bottle
  Manual shoot button added
  More accurate targeting system
  Integration of Telegram
  Included website

## Slide 8
How Our Work Differs | Author / Year | Work Done | Gap Identified
We embed YOLOv8/v11 inside a closed-loop CPS with servo + Telegram alerts. | Redmon et al., 2016 | Introduced YOLO — a single-stage real-time object detection architecture. | Generic detector — no integration with physical actuators or alert systems.
We deploy YOLO on CPU + Arduino | Sohan et al., 2024 | Reviewed YOLOv8 — benchmarked accuracy and speed against v5/v7. | Survey only; no deployment on resource-constrained edge hardware.
We add servo-aimed response + manual override for active defense. | Springer, 2024 | YOLOv8 smart surveillance CCTV system, reporting 96% detection accuracy. | Passive monitoring only — no physical response or actuation layer.
Our YOLO layer classifies targets and ignores persons (green/red logic). | IJSAT, 2025 | Survey of Arduino-based defense radars using ultrasonic + servo turrets. | Ultrasonic detects all obstacles — cannot classify threat vs. safe object.
8
Literature Review

## Slide 9
SOFTWARE TOOLS USED
  Simulink
  Python
  YOLOv11 Object Detection
  OpenCV
  Embedded Control Programming
  Processing
Dataset Used
Custom dataset trained for:
  Phone
  ID card
  Water bottle
9

## Slide 10
HARDWARE COMPONENTS USED
  Camera Module
  Microcontroller (Arduino)
  Servo Motor
  Ultrasonic Sensor
  Power Supply
10

## Slide 11
11
System Architecture

## Slide 12
12

## Slide 13
Working Methodology
The proposed system operates through a combination of computer vision, sensor detection, and mechanical actuation. The overall working process is explained in the following steps.
1. Object Monitoring
  The camera module continuously captures real-time video of the surrounding area. The video frames are sent to the processing unit for analysis.
2. Image Processing
  Each frame from the camera is processed using YOLOv11 object detection algorithm. The model analyzes the image and identifies objects present in the frame.
3. Object Detection and Classification
The YOLOv11 model detects and classifies only the trained objects, which include:
  Mobile Phone
  ID Card
  Water Bottle
When any of these objects are detected, the system highlights them with bounding boxes and identifies their position in the frame.
13

## Slide 14
Working Methodology
4. Target Position Identification
After detection, the coordinates of the detected object are obtained from the model output. These coordinates are used to determine the direction in which the system must move to align with the object.
5. Servo Motor Control
The detected target position is sent to the microcontroller, which controls the servo motor. The servo motor rotates to align the shooting mechanism toward the detected object.
6. Manual/Auto Shooting Mechanism
Once the target is aligned, the system waits for user confirmation if in manual mode.
A manual shoot button is provided, and when pressed, it activates the trigger mechanism to perform the shooting action. Else in auto mode it fires immediately after detecting the target without any delay.
14

## Slide 15
15
Simulink- Object out of range

## Slide 16
16
OBSERVATIONS

## Slide 17
17
Simulink Object in range

## Slide 18
18
OBSERVATIONS

## Slide 19
Remote Monitoring via Telegram Bot
What it does:
  On confirmed target fire → sends instant Telegram message with timestamp
  Automatically captures and sends a .jpg photo of the target
  Enables remote operator awareness even when away from the system
How it works (from your code):
TARGET DETECTED → FIRE CONFIRMED
↓
save target_{timestamp}.jpg
↓
POST /sendMessage → "🚨 TARGET ELIMINATED"
POST /sendPhoto → Target image attached
Why it matters: Adds a real cyber-physical systems layer — physical event triggers digital notification, closing the CPS feedback loop your course focuses on.
19

## Slide 20
20
RADAR

## Slide 21
21
Results
  System successfully detects:
  Mobile Phones
  ID Cards
  Water Bottles
  Advantages
  More accurate than ultrasonic-only system
  Vision-based detection
  User controlled firing

## Slide 22
22
Limitations & Future Enhancements
Limitations:
  Detection accuracy drops in low-light or occluded conditions
  YOLO runs on CPU — causes latency (~200-400ms per frame)
  Fixed camera FOV limits detection range
  System depends on USB serial; wireless control not yet implemented
  Custom-trained model (best.pt) still needs more training data for ID cards
Future Enhancements:
  GPU acceleration (your gpu.py already checks for CUDA — wire it in!)
  Pan-tilt dual-axis servo for full 2D tracking
  Upgrade to custom-trained YOLOv11 model replacing COCO classes
  Add night-vision / IR camera support
  Expand Telegram integration to include live video stream alerts

## Slide 23
23
Conclusion
The proposed system integrates YOLOv11-based object detection with a camera module and servo control to create an improved smart detection mechanism. The system successfully identifies specific objects such as mobile phones, ID cards, and water bottles in real time. Compared to the previous ultrasonic-only system, this approach provides more accurate and intelligent detection. The addition of a manual shoot button ensures better control and safety during operation. Overall, the project demonstrates the effectiveness of combining AI-based vision systems with embedded hardware for security applications.

## Slide 24
THANK YOU
24